## Slide 1: ENGI 301 Clap on LED Lights Proposal
10/5/21
Haruto Sasajima

## Slide 2: Background Information
  Motivation
  LED light strips are a popular way to liven up a dull dorm room. My room currently has some installed and are controlled by a small remote. However, I frequently lose my remote, hindering my ability to turn on my LEDs. Being able to turn on and off my LEDs from anywhere around my room by just clapping would remove the need for a remote and save time. Additionally, most LED strips I've seen are only able to uniformly display one color at a time, leading to a lack of variety in terms of color patterns.
  Proposal
  Make a system in which I can clap to turn my LEDs on and off. The LEDs in my LED strip are able to be individually coded, meaning they will be able to display multiple colors in different patterns at once. This design features a unique clap-on clap-off mechanism, as well as a warm colors, cool colors, and rainbow LED color pattern setting. These features will contribute to a unique user experience that I have not seen with LED lights that I have previously owned.
  Features:
  Turned on/off using clap
  Double clap for strobe light
  Different color/pattern settings using buttons
  Dims or brightens based on ambient light level

## Slide 3: System Block Diagram
PocketBeagle
USB A Microphone
LED Light Strip
Level Shifter
(TXS0108E)
USB Hub
Micro USB Port
Button
GPIO (P2.02)
GPIO (P2.04)
GPIO (P2.06)
Button
Button
GPIO (P1.08)
USB1

## Slide 4: Power Block Diagram
PocketBeagle
USB A Microphone
LED Light Strip
(5 V)
Level Shifter
(TXS0108E)
(5 V)
(Up to 100mA)
USB Hub
(5V)
(Up to 900mA)
Micro USB Port
Button
(3.3 V)
SYS 3.3V (P1.14)
SYS 3.3V (P1.14)
SYS 3.3V (P1.14)
Button
(3.3 V)
Button
(3.3 V)
SYS 3.3 (P1.14)
VIN (P1.07)
3.3 V
3.3 V
3.3 V
5 V
VCCA, OE
VCCB
3.3 V
5 V
5 V

## Slide 5: Components / Budget
Component | Need to Buy | Cost
PocketBeagle | owned | N/A
Micro USB port | owned | N/A
LED Light Strip | 1 | $19.99
Breadboard | owned | N/A
Level Shifter (TXS0108E) | 1 | $1.28
Jumper cables | owned | N/A
Button | owned | N/A
Micro USB to USB A adapter | owned | N/A
USB A mini microphone | 1 | $7.98
Ambient Light Sensor: https://www.sparkfun.com/products/8688 | 1 | $4.50
USB Hub | 1 | $17.99
USB A to 5 pin terminal block adapter | 1 | $4.95
1k Ohm Resistors | owned | N/A